## Slide 1: Food Preservation
Prepared by Marie Anderson
Mapleton Ready

## Slide 2
Why preserve food?

## Slide 3
I’ve canned this way for years and no one has died yet!
That may be true but . . .!
Notes: I’ve canned this way all of my life and no one has died yet!

## Slide 4: Food Safety is Our #1 Priority!
Canning is NOT Cooking!
  Successful Cooking = Good tasting food w/ expected consistency
  Successful Canning = Control of potentially harmful microorganisms
    Appearance, taste, texture not always good indicators

## Slide 5
A sealed jar does not mean a safe jar
  Enough heat must reach center of jar to control molds, yeasts, or bacteria that might cause illness
  MUST be enough time for the heat to penetrate the food and eliminate undesirable microorganisms.
Processing Time Scientifically determined
  Researchers repeat process over and over until they can guarantee control of the target microorganism.
Jars do not need to be sterile. Clean is good.

## Slide 6
Use Current, Tested Recipes
            USDA Canning Guide
            Current Ball Blue Book
                www.freshpreserving.com
            So Easy to Preserve
                www.nchfp.uga.edu
Notes: BE CURRENT:
  Test dial gauge each year
  Call local Extension office and ask if there are new canning guidelines
USE TESTED research-based recipes – these recipes have been tested repeatedly in labs to control for microorganism growth
  USDA Complete Guide to Home Canning
  Ball Blue Book
Control your creativity when canning

## Slide 7
Factors affecting processing times:
            Acid content of the food
            Density of the food
            Altitude
            Starting Temperature of the Food
            Size – quarts or pints

## Slide 8
Molds & Yeasts
Process at 212° F in Boiling Water Bath
  (Kills Molds & Yeasts in High-acid Foods)
Cut off point = 4.6↓
Bacteria
Process at 240° F in Steam Pressure Canner
  (Kills anaerobic organisms like those that cause botulism in low acid foods)
ACID CONTENT OF FOOD

## Slide 9
Botulism Toxin
It is when the botulism spore is placed in an environment with
  Low acidity (pH is greater than 4.6)
  Moisture (and it doesn‘t take much!)
  And no oxygen
that it creates a toxin that is deadly!
When we home can low-acid foods, we have just created the PERFECT environment for botulism to kill us (if it is not killed)!

## Slide 10: Killing Botulism
It is impossible to reach 240° F in a regular boiling water bath canner. The highest possible temperature we can reach is 212° F (the boiling point of water at sea level).
In order to kill botulism, we must use a pressure canner when we home-can any meats or vegetables (that aren’t pickled).
  With pickled vegetables, if we follow an approved recipe, we add enough acid (i.e., vinegar) to make it safe from botulism.

## Slide 11: Density: Heat Penetration impacted by thickness of contents
Heat must travel from molecule to molecule to center of the jar and is a slow process.
Heat travels through convection currents which circulates to bring heat to the center of the jar.
Conduction:
Thick/solid contents
Convection:
Liquid/Less dense contents
Notes: Changing density:
Changing a recipe will alter the density of the product. Give examples: simmering salsa, adding thickeners, adding more solids
Altering density impacts processing time.
Want it thicker, add thickener just before serving.

## Slide 12: Adjusting for Altitude
Water boils at 212°F at sea level
At higher altitudes, water boils at lower temperatures – for example: between 4,000 and 6,000 feet, water boils from 204°F to 201°F.
This means it takes longer to heat the center of the jar to the necessary temperature to kill molds/yeast (high-acid) and botulism (low-acid).
A little side-note for any candy-makers out there... You also need to apply altitude adjustments to your candy thermometer to have the best results!
Source: USDA Complete Guide to Home Canning, revised 2009

## Slide 13: Processing Time
As Altitude Increases
  ADD:
TIME (Boiling Water Canner)
  add 10 min. for 3,000-6,000 ft.
  OR
PRESSURE (Pressure Canner)
  Dial gauge: 15 lbs. at 4,001-6,000 ft.
  Weighted gauge: 15 lbs. at 4,001-6,000 ft.
ALWAYS verify according to guidelines

## Slide 14
Equipment
Notes: Canners including electric water bath
Talk about steam canners
Jars
Lids – types
Funnels, jar lifters, wands

## Slide 15: Steam Canners
Use current research-tested recipes developed for a boiling water canner.
Temperature must be monitored to ensure the process only begins when the temperature reaches the boiling point.
Jars must be heated prior to filling.
Adjust time for altitude.
Processing time should be limited to 45 minutes or less.
Do not open the canner to add water during the process. This may impact the temperature and food may be under processed.
Must only be used with these recommendations:

## Slide 16: Smooth Top Ranges
Contact range manufacturer before pressure canning.
Water bath canners must be designed for smooth top ranges or large, deep, flat-bottomed stockpots no larger than the cooking surface.
Portable gas burners (i.e. Camp Chef) (not recommended)
    BTU’s must be under 12,000
    May cause canner/property damage
    Susceptible to flame being blown out
    May run out of gas before processing time is complete
Ball now has an electric water bath canner!

## Slide 17
Packing Methods
Raw pack
  Raw food put into jar; then boiling canning liquid is poured in over food.
  Oxygen in food tissue may cause discoloration after 2 to 3 months
  More suitable for vegetables processed in a pressure canner
  Fruits (high air content) will float in jars

## Slide 18
Hot pack
  Boil raw foods and canning liquid 3 to 5 minutes in a saucepan or blancher, then poured into jars.
Advantages
  Helps remove air from food tissues
  Helps keep the food from floating in the jars
  Increases vacuum in sealed jars, and improves shelf life.
  Preshrinking food permits filling more food into each jar.
Packing Methods

## Slide 19: Jars & Lids
Fill jars w/food, leaving correct headspace.
Remove air bubbles with a rubber spatula.
Wipe down mouth of jar.
Follow lid manufacturer’s recommendation for preparing & tightening lids.
  Too tight: air can’t escape, buckling, food discoloration and jar breakage
  Too loose: liquid escapes, seal fails.
  DO NOT readjust the lid after processing!
Notes: How to test lids
Tattler lids

## Slide 20
Headspace
Headspace is the unfilled space between the food in the jar and the lid.
  Jams & Jellies ¼-inch
  Tomatoes, fruits, pickles ½-inch
  Most low acid foods 1-inch to 1¼-inches
Headspace is needed because foods expand as the jars are heated.
Notes: The air in the food, starch content and processing temperature determines how much a food will expand.
The higher the temperature the greater the expansion.
Starchy foods such as as corn, potatoes, lima beans and rice expand and absorb water during heat processing.
Too little – food may expand and bubble out and prevent sealing
Too much – food at the top may discolor and may not seal properly because there will not be enough processing time to drive all the air out of the jar.

## Slide 21: Boiling Water Canner
Fill canner halfway with water.
Preheat to 140°F for raw pack and 180°F for hot packed foods.
Load filled jars with lids into rack and then lower into water.
Add more boiling water until at least 1inch over tops of jars.
Cover; turn heat to highest setting until water boils vigorously.

## Slide 22: Pressure Canner
Vent at least 10 minutes before pressurizing.
For altitudes above 1,000 feet the pressure must be adjusted: Utah County = 15 lbs.
Gauges should be checked before use each year.
Check gaskets. Nicked or dried gaskets could result in steam leaks.

## Slide 23: Pressure Canner
Put 2-3 inches of water in canner, place filled jars with lids into the canner and fasten cover securely.
Heat until steam escapes from vent port.
Let steam vent for 10 minutes, then place weight on vent port or close petcock. Allow to pressurize.
Begin to time when recommended pressure is reached.
Adjust heat to regulate a steady pressure on gauge (can be slightly above)

## Slide 24: Pressure Canner
When time is up, turn off heat & let canner depressurize. DO NOT force-cool canner – Can result in damage & food spoilage.
After canner is depressurized, remove weight from vent. Wait 10 minutes, remove lid & avoid steam.
Allow jars to sit for 5 minutes before removing.
Remove jars and place on towel or rack away from drafts.

## Slide 25: Cooling Jars
DO NOT retighten lids.
Cool at room temperature for 12-24 hours on a rack or a towel.
When cooled remove screw lid, wash, dry (bottles & screw bands), label jars & store.
If lids do not seal, reprocess within 24 hours.
Reprocess for the entire processing time.
Or refrigerate the jars and consume within 2-3 days.

## Slide 26: Storing Your Food
Label and date your jars.
Store filled jars in clean, cool, dark and dry place.
Accidental freezing may cause unsealing or softening of food. Insulate jars if they are stored in a place with possible freezing capabilities.